## Slide 1: A Near Term Solution for Home IP networking (HIPnet)
draft-grundemann-homenet-hipnet
RIPE 66 – Dublin – 14 May 2013
Chris Grundemann, Chris Donley,
John Brzozowski, Lee Howard, Victor Kuarsingh

## Slide 2: Yesterday’s Home Network
Home LAN 2
Home LAN 1
Internet Service Provider
Wi-Fi Range Extension
NAT
NAT

## Slide 3: Emerging use cases for the home network
Separation of guest users from home users
Community Wi-Fi
  Wi-Fi GW in the subscriber home is used to provide Wi-Fi roaming services
Femto cell
  GW in the subscriber home is used to provide cellular services
Smart grid
Security, Monitoring, & Automation
Multi-homing
Video content sharing and streaming between the devices inside the home
IP video streaming from the internet
Telecommuting and corporate IT requirements (e.g. network separation)
Ever increasing devices in the subscriber home
Emergence of Heterogeneous link layer technologies (e.g. low powered sensor networks) with different requirements

## Slide 4: Tomorrow’s Home Network
Home LAN 2
Home LAN 1
Internet Service Provider
Wi-Fi Range Extension
Multiple SSIDs: Private, Guest, Community, ISP Branded, Etc.
Guest LAN
Home LAN 4
ZigBee Network
Home LAN 3
Home Automation Gateway
IP Sensor Gateway
Home Entertainment Gateway
Key assumption: Home users will not be configuring advanced networks

## Slide 5: HIPnet is a Solution to Complex Home Networks
A self-configuring home router architecture
  Capable of operating in increasingly large residential home networks
  Requires no user interaction for the vast majority of use-cases
  Uses existing protocols in new ways
  Does not require a routing protocol
  Meets the principles of draft-ietf-homenet-arch

## Slide 6: Common Principles Guide HIPnet
Home networks will become more complex, home users will not
Invoking a god box leads to religious wars
New protocols bring new problems
We have enough addresses
Use IPv6, support IPv4

## Slide 7: HIPnet Meets Current Needs with Existing Functionality
IPv6 is being deployed today (thankfully)
Home networks are growing today
A solution is needed today (or sooner)
  Based on RFC 6204/bis
HIPnet works: running code
  Built on OpenWRT
  Updates to DHCP

## Slide 8: HIPnet Works
Self-Organizing: Directionless Routers
Addressing: Recursive Prefix Delegation
Routing: Hierarchical Routing
Bonus: Multiple Address Family Support
Supports arbitrary topologies, multihoming, security, and service discovery…
Notes: Self-Organizing: Directionless Routers
  No user interaction required for most use cases
Addressing: Recursive Prefix Delegation
  Uses existing protocol (DHCP-PD)
Routing: Hierarchical Routing
  No routing protocol required
Bonus: Multiple Address Family Support
  Uses IPv6 to configure IPv4

## Slide 9: Directionless Home Routers
The HIPnet router sends Router Solicitations on all interfaces (except Wi-Fi*)
The router adds any interface on which it receives an RA to the candidate 'up' list
The router initiates DHCPv6 PD on all candidate 'up' interfaces.
  If no RAs are received, the router generates a /48 ULA prefix
The router evaluates the offers received and chooses the winning offer as its Up Interface

## Slide 10: Deterministic Up Interface Selection Criteria
Valid GUA preferred (preferred/valid lifetimes >0)
Internal prefix preferred over external (for failover - see Section [6.1])
Largest prefix (e.g. /56 preferred to /60)
Link type/bandwidth (e.g. Ethernet vs. MoCA)
First response (wait 1 s after first response for additional offers)
Lowest numerical prefix

## Slide 11: Example Up Detection
R1
R2
R3
RS
RA
DHCP Req.
Offer
ULA
GUA
ULA
GUA
GUA
GUA
“UP”
Default route

## Slide 12: More Complicated Up Detection Example
R1
R2
R3
R4
Internet
PD req.
/60
/64
/64
UP

## Slide 13: Directionless Routers Example: Rearranging the Network
R1
R2
R3
R4
Internet
RS
RS
RA
No RA
UP
UP
Also, see following slides for case where R4 ends up on same LAN as R1, R2, R3

## Slide 14: HIPnet Creates a Logical Hierarchy from a Physically Arbitrary Network
Internet Service Provider
R1
R2
R3
R4
R5
Physical Connection
IP Connection

## Slide 15: Recursive Prefix Delegation
Home LAN 2
Home LAN 1
Internet Service Provider
Guest LAN
Home LAN 4
ZigBee Network
Home LAN 3
Notes: Based on DHCPv6 prefix delegation
  RFC3633
Inspired by a “Simple Approach to Prefix Distribution in Basic Home Networks”
  draft-chakrabarti-homenet-prefix-alloc
HIPnet router receives prefix in IA_PD, breaks it up, and hands it out

## Slide 16: Width Optimization
If the received prefix is smaller than a /56
  8 or more port routers divide on 3-bit boundaries (e.g. /63)
  7 or fewer port routers divide on 2-bit boundaries (e.g. /62)
If the received prefix is a /56 or larger
  8 or more port routers divide on 4-bit boundaries (e.g. /60)
  7 or fewer port routers divide on 3-bit boundaries (e.g. /59)

## Slide 17: Hiearchical Routing Table
Up
Down
::/0  Default Router
IA_PD  Downstream IR’s “Up Interface” IP
Notes: CER on the LAN side will have an additional GUA- ULA binding

## Slide 18: Multiple Address Family Support
Recursive prefix delegation can be extended to support additional address types
  ULA, additional GUA, or IPv4
8 or 16 bit Link ID extrapolated from IA_PD
  Bits 56-64 or 48-64
Additional prefixes are prepended to Link ID
  Additional prefixes extrapolated from RA or DHCPv4 on Up Interface

## Slide 19: Link ID
GUA IPv6 Address
48b - ISP
64b – Interface ID
16b – Link ID
48b - ULA
IPv4 “10.”
/64
/24

## Slide 20: Multihoming Use-Cases
Special purpose IP connection (e.g. IP Video)
Backup connection (i.e. active/standby)
“True” multihoming (i.e. active/active)
(Info in backup slides)

## Slide 21: The HIPnet Solution
Directionless Home Routers
  Up Detection creates logical hierarchy
Recursive Prefix Delegation
  Link ID allows multiple address families
Hierarchical Routing
  Determinism without a routing protocol
The next step in home networking!

## Slide 22: Questions?
@ChrisGrundemann
chris@chrisgrundemann.com
http://chrisgrundemann.com

## Slide 23: Appendix
Backup Slides

## Slide 24: Recursive Prefix Delegation
Based on DHCPv6 prefix delegation
  RFC3633
Inspired by a “Simple Approach to Prefix Distribution in Basic Home Networks”
  draft-chakrabarti-homenet-prefix-alloc
HIPnet router receives prefix in IA_PD, breaks it up, and hands it out

## Slide 25: HIPnet Addressing Details
The HIPnet router acquires a prefix and then breaks it into sub-prefixes
The first of these sub-prefixes is further broken into /64 interface-prefixes for use one on each of the router’s down interfaces
  If the sub-prefix is too small to number all down interfaces, the router uses additional sub-prefixes as needed (in numerical order)
  If the aggregate prefix is too small to number all down interfaces, the router collapses them into a single IP interface, assigns a single /64 to that interface
The remaining sub-prefixes are delegated via DHCPv6 to directly downstream routers as needed, in reverse numerical order

## Slide 26: Hierarchical Routing
The HIPnet router installs a single default 'up' route and a more specific 'down' route for each prefix delegated to a downstream IR
‘down' routes point all packets destined to a given prefix to the WAN IP address of the router to which that prefix was delegated
No routing protocol needed!

## Slide 27: Multihoming Use-Cases
Special purpose IP connection (e.g. IP Video)
Backup connection (i.e. active/standby)
“True” multihoming (i.e. active/active)

## Slide 28: Special Purpose IP Connection
IP video or other non-Internet connection
Some configuration allowed
  User or technician configured
  Managed or semi-managed
Automated / configurationless
  Has been discussed
  Outside of current scope
    May be included in future versions of HIPnet

## Slide 29: Backup Connection
Active/standby with failover
Default HIPnet use-case
Internal prefix preferred in Up detection
  First CER to come online is primary
  Backup CER doesn’t announce its prefix
  Upon failure of primary, secondary CER announces its prefix (becomes primary), tree is re-built
  Backup judges failure based on:
    Timeout (primary CER stops advertising GUA)
    Preferred, valid, & router lifetimes from primary set to 0

## Slide 30: Backup Network – Example
R1
R2
R3
R4
Internet
LTE
RAs

## Slide 31: Multihoming
Active/Active with load sharing
Possible under HIPnet architecture
“Shared tree”
  Primary CER (first active) builds hierarchical tree
  Secondary CER adds its prefix to existing tree
  Secondary can be same level (full multihoming) or lower level (VPN use-case)
  Requires NAT or source routing at CERs

## Slide 32: Multihoming Algorithm
CER performs prefix sub-delegation as described earlier
  hierarchical tree network
Secondary CER (R4) obtains second prefix from ISP2
  Advertises ISP2 prefix as part of RA
  Includes sub-prefixes from both ISPs in IA_PD (same “link id”)
Secondary CER points default route to ISP2, internal /48 route to upstream internal router (e.g. R1)
Devices below R4 (e.g.R3, R5) use ISP2, but have full access to all internal devices using ISP1 prefix or ULAs
  If ISP2 link fails, traffic flows to ISP1
Devices not below R4 (e.g. R1, R2) use ISP1, but have full access to all internal devices using ISP1 prefix or ULAs
Potential optimization - CER source routing – default route selected based on packet Source IP address

## Slide 33: Multihoming Network Example
ISP1
R1
R2
R3
R4
ISP 2
(CER)
DHCP
RA
RA
RA
RA
R5

## Slide 34: VPN Multihoming Example
Internet Service Provider
R1
R2
R3
R4
R5
ISP 2

## Slide 35: Multihoming FAQ
What if the PD sizes from ISP1 and ISP2 are different?
  The hierarchy determined by DHCP (ISP1 in the example)
    Clarifying rule: routers MUST NOT act as DHCP client and server on same link.
What if the L2 router picks the wrong L1 for default traffic?
  The wrong L1 forwards it to the right L1
What if we don’t use the PD algorithm discussed above?
  Not guaranteed to work
    Routers only receive PD from one DHCP server
    Would require mechanism for sending ISP2 PD to the CER
Notes: Subscriber has primary ISP connection to an ISP
Subscriber may have a secondary connection e.g. for work VPN, video network, etc.
  Devices connected to secondary network access Internet through secondary ISP
  Devices still have access to all network resources in the home
  Devices can use primary ISP if secondary fails
  Other devices do NOT use second ISP

## Slide 36: Multicast Requirements
HIPnet routers support service discovery through multicast forwarding
Simple rules:
  MULTI-1: A HIPnet router MUST discard IP multicast packets that fail a Reverse Path Forwarding Check (RPFC).
  MULTI-2: A HIPnet router that determines itself to be at the edge of a home network (e.g. via CER_ID option, /48 verification, or other mechanism) MUST NOT forward IPv4 administratively scoped (239.0.0.0/8) packets onto the WAN interface.
  MULTI-3: HIPnet Routers MUST forward IPv4 Local Scope multicast packets (239.255.0.0/16) to all LAN interfaces except the one from which they were received.
  MULTI-4: A HIPnet router that determines itself to be at the edge of a home network (e.g. via CER_ID option, /48 verification, or other mechanism) MUST NOT forward site-scope (FF05::) IPv6 multicast packets onto the WAN interface.
  MULTI-5: HIPnet routers MUST forward site-scoped (FF05::/16) IPv6 multicast packets to all LAN interfaces except the one from which they were received.
  MULTI-6: A home router MAY discard IP multicast packets sent between Down Interfaces (different VLANs).
  MULTI-7: HIPnet routers SHOULD support an IGMP/MLD proxy, as described in [RFC4605].

## Slide 37: Security & NAT Requirements
SEC-1: The CER MUST enable a stateful [RFC6092] firewall by default.
SEC-2: HIPnet routers MUST only perform IPv4 NAT when serving as the CER.
SEC-3: By default, HIPnet routers SHOULD configure IPv4 firewalling rules to mirror IPv6.
SEC-4: HIPnet routers serving as CER SHOULD NOT enable UPnP IGD ([UPnP-IGD]) control by default.

## Slide 38: IR Security Options
Filtering Disabled
Simple Security + PCP
Advanced Security [I-D.vyncke-advanced-ipv6-security]